## Slide 1: RV-9A 90577 Avionics/Electrical

## Slide 2: Disclaimer
It’s only perfect until you fly it,
Then you’ll want to change it.
… or build another airplane!
  (George McNutt)

## Slide 3: Degree of Difficulty
Designing and wiring an airframe and panel is difficult, but achievable.
Read the references, and get help.
Start with a completed design and have a design review.
  Find an experienced builder or avtech to help
  Use the same person to consult with you through the tough parts.
  You will save a lot of money, time and frustration.

## Slide 4: Define the Mission
Basic VFR
Night VFR
VFR OTT
Day IFR
Night IFR
Equipment list is available in the CARS on Transport Canada web site:
  http://www.tc.gc.ca/CivilAviation/RegServ/affairs/cars/menu.htm
Allow for upgrades (VFR-OTT to IFR?)
I decided on Night/VFR OTT

## Slide 5: Select the Equipment

## Slide 6: All-Electric or Electric/Vacuum?
Many new certified aircraft are going all electric, even for full IFR.
All-electric is lighter, cheaper and more reliable
But is prone to a single-point failure…. Alternator/Battery
Consider a stand-by alternator or backup battery strategy.
Or you could use a vacuum system

## Slide 7: Failure Considerations
If it ain’t installed, it has zero weight, requires no maintenance, is free and will never break.
Consider failure mechanisms:
  primary electric failure
  individual instrument failure
Have redundancy or backups
  EFIS is backed up with ASI, TC, Compass, Stall indicator and GPS virtual instruments.
Internal backup batteries for EFIS and GPS and Engine Monitor. Handheld Comm.

## Slide 8: Avoid $$God-Boxes
Glass cockpit displays are great, but….
  They are expensive and big
  you need two of them
  and you need a backup electrical system
The fewer functions in a box, the easier it is to provide a back-up
  e.g. separate fuel level gauges backs up fuel totalizer in engine monitor.

## Slide 9: Select the Equipment
Budget is always a consideration
Simplicity of installation is very important
For example
  Garmin AT SL-40 COMM has a dual-watch function, allowing you to listen to two frequencies at once and transmit on one
  Saves the weight, panel space and extra antenna of two separate comms.
  Maybe not cheaper because the SL-30 is about twice the price of two cheap comms.
Consider buying new
  New avionics are much more reliable than older, refurbished stuff.
  Lighter, lower power, less panel space as well.

## Slide 10: Design the Panel
Start with the Panel Designer program on line: www.epanelbuilder.com
Van’s has a full size Autocad file of the panel blank!
  http://www.vansaircraft.com/public/downloads.htm
This can be read by many CAD programs.
Do all you design on the computer first.
Measure for interfering parts on the aircraft structure and mark keep-out areas on the blank.
Paper dolls work… you can find a lot of problems pretty quickly.
It can take dozens of attempts to settle on what you want.

## Slide 11: Final Panel

## Slide 12: Design the Electrical System
Lights, heated pitot, strobe system, alternator/battery system
Connectors: wing-root disconnect, panel disconnect
Start with the Aeroelectric Connection on-line! www.aeroelectric.com
Use AC 43.13 as a reference for wire gauge, breaker/fuse selection and grounding techniques.
Find a schematic design program: www.expresspcb.com
Start with someone else’s design
Get advice

## Slide 13: Getting Started
Order the main electrical system parts… wire, terminals, lights, strobes, tie-wraps (about 2000 will do)
www.steinair.com, www.aeroelectric.com, www.digi-key.ca, www.creativair.com, www.wicksaircraft.com, www.aircraftspruce.com,

## Slide 14: Wires & Terminals
Use Mil-spec Tefzel insulated wiring
  never use automotive (PVC) wiring!
  Can burn and emit poisonous fumes
Terminals
  crimp terminals.
    fast-ons, ring terminals
    fast-ons not common in certified aircraft, but are used.
    Crimping is reliable and gas-tight

## Slide 15: Fuses or Breakers
Both work
Fuses are cheaper
Breakers are easier to wire and indicate when tripped.
Polyfuses may be used, but they are not certified.

## Slide 16: Switches
Toggle or Rocker?
Toggle are easier to mount, are very tactile and positively indicate their position
Rockers can be backlit or labeled easily

## Slide 17: Cockpit/Panel Lighting
Most avionics have built-in backlights
You can add light rings, post lights or flood lights.
A map light is a great addition
Van’s sells a nice little dimmer module for $20.00

## Slide 18: Wire Grooming
String ties
  if you really want to impress the judges
Tie-wraps
  easy to use, easy to change
  you need about 2000 (1800 end up in the garbage)
Cushion clamps
  Used to secure wiring bundles and prevent chafing
Split tubing
  split polyethylene tubing lengthwise and glue onto sharp edges to prevent chafing.
Coax
  do not clamp tightly, it will affect the performance of the cable.
Wire marking (if you don’t own a $3000 marking machine)
  buy fabric label strips from www.steinair.com
  wire marking is a pain, but well worth it later on.

## Slide 19: Wire Routing
Avoid running antenna coax in long wiring bundles.
Don’t run transponder cable parallel to any other wire or coax.
Put some slack in the ELT antenna cable.
Secure with cushion clamps around interfering structures.

## Slide 20: Grounding
Firewall grounding bus for all power connections.
  Every circuit has a separate ground return.
  Prevents electrical interference.
Do not use the airframe as a power ground.
  It is acceptable to use the wing spars as a ground return for wing wiring
    I ran a ground wire from the spars to the firewall.
Shielded wire grounds can be grounded to the airframe/panel at one end only
  Don’t use the shield to carry power.

## Slide 21: Tools
Wire strippers
Wire cutters
Crimp tools (d-sub, fast-on, coax, box)
Crimp pin removal tools
Dental probes
Soldering iron
DVM/Beeper
Tie-wrap gun
Heat-shrink tubing and heat gun

## Slide 22: Supplies
Heat shrink tubing
Dielectric grease
  apply to connectors, terminals (long lasting)
ACF-50, Corrosion-X
  apply to connectors, terminals (24 months)
Aluminum washers
Lock washers (split ring and star)